Software architecture for autonomous Robobot
J. Christian Andersen

---
Robobot
Software architecture and
introduction to software
J. Christian Andersen

---
Robobot
Introduction to software
Level 1
J. Christian Andersen

---
Robobot
Introduction to software
Level 3 – Situation / vision
J. Christian Andersen

---
Robobot
Introduction to software
Level 2 – Drive alternatives
J. Christian Andersen

---
Robobot
introduction to C++ software
J. Christian Andersen

---
Robobot
introduction to C++ Plan100
J. Christian Andersen

---
Robobot
Line sensor code and calibrate
J. Christian Andersen

---
Robobot
Edge and distance code
J. Christian Andersen

---
Robobot in blocks
Motor
Distance
Distance
Battery
12V
Servo
PWM
5V
on
Wifi
Raspberry PI
Mission control
Teensy board
(Regbot)
encoder
USB
USB
Camera
PWM
encoder
5V
display
digital
Motor
pulse
analogue
Digital IO
IMU
Line sensor
start

---
Robobot software blocks
Camera
USB
Raspberry PI (3 or 4)
Teensy PCB (Regbot)
Wifi
display
Sensor
Interface
Publish/
Subscribe:
Encoder,
IMU,
IR-distance,
line-sensor
battery,
current
...
Python3
(socket-base-py)
Base control
(raubase C++)
/dev/ttyACM0
USB
Servo interface
IP-display
(ip_disp)
Motor interface
Start button only
Digital IO
start
start

---
Camera
USB
Raspberry PI (3 or 4)
Wifi
Python3
(socket-base-py)
Base control
(raubase C++)
/dev/ttyACM0
IP-display
(ip_disp)
Start button only
Digital IO
start
Software on Raspberry Pi
start

---
Architecture description – NASREM
(text in boxes are just to exemplify)
hours
minutes
seconds
milliseconds
ref: NASREM
The National Aeronautics and Space Administration (NASA) and the US National Institute of Standards and Technology (NIST) have developed a Standard Reference Model Telerobot Control System Architecture (NASREM). Albus, J. S. (1992), A reference model architecture for intelligent systems design.
Update frequency
Real time requirement
Planning horizon
Abstraction
Situation
sensor
Situation
detect
Situation
behaviour
Move type
control
Drive
methods
Drive
sensing
Pose
sensing
Robot
pose
Drive
control
sense
Drive system
Operator interface (debug)
Objectives
Sensory
processing
Modelling and
assessment
Behaviour
generation
Configuration

---
(version for the rsewiki)
Robobot level 1 (velocity and heading)
Sensory
processing
Modelling
Plan and execute
Plan
Heading mode
Forward velocity
Rotation velocity
Forward velocity
Rotation velocity
Mixer
(cmixer)
Heading
(cheading)
Encoder
(sencoder)
Pose
(mpose)
Velocity
(cmotor)
PID
(upid)
Logfiles
(for Matlab)
Parameters
(uservice)
Config.
(robot.ini)
Teensy i/f
(steensy)
USB
Hardware
(Teensy)
Most block text in brackets
corresponding to filenames
(eg. upid = upid.cpp and upid.h)
Sensor data
(text lines)
Motor voltage
(text lines)
Situation
sensor
Situation
detect
Situation
behaviour
Drive type
control
Drive
methods
Drive
sensing
Pose
sensing
Robot
pose
Drive
control
sense
Drive system
Sensory
processing
Modelling and
assessment
Plan and
execute

---
Behaviour plans
(version for the rsewiki)
Robobot level 2 (drive alternatives)
Sensory
processing
Selected
Drive type and
parameters
Modelling
Behaviour generation
Distance
(sdist)
Distance
(mdist)
Wall drive
(cdist)
PID
(upid)
Line sensor
(sedge)
Edge detect
(medge)
Edge drive
(cedge)
PID
(upid)
Parameters
(uservice)
Logfiles
(for Matlab)
Gyro/acc
(simu)
Tilt
(mimu)
Config.
(robot.ini)
Forward velocity
Rotation velocity
Heading mode
Most block text in brackets
corresponding to filenames
(eg. upid = upid.cpp upid.h)
---- Dashed frame means
not provided.
Teensy i/f
(steensy)
Pose
(mpose)
drive
control
Level 1
Situation
sensor
Situation
detect
Situation
behaviour
Drive type
control
Drive
methods
Drive
sensing
Pose
sensing
Robot
pose
Drive
control
sense
Drive system
Sensory
processing
Modelling and
assessment
Plan and
execute

---
Behaviour plans
(version for the rsewiki)
Robobot level 2 (drive alternatives)
Sensory
processing
Selected
Drive type and
parameters
Modelling
Behaviour generation
Distance
(sdist)
Distance
(mdist)
Wall drive
(cdist)
PID
(upid)
Line sensor
(sedge)
Edge detect
(medge)
Edge drive
(cedge)
PID
(upid)
Parameters
(uservice)
Logfiles
(for Matlab)
Gyro/acc
(simu)
Tilt
(mimu)
Config.
(robot.ini)
Forward velocity
Rotation velocity
Heading mode
Most block text in brackets
corresponding to filenames
(eg. upid = upid.cpp upid.h)
---- Dashed frame means
not provided.
Teensy i/f
(steensy)
Pose
(mpose)
drive
control
Level 1
Situation
sensor
Situation
detect
Situation
behaviour
Drive type
control
Drive
methods
Drive
sensing
Pose
sensing
Robot
pose
Drive
control
sense
Drive system
Sensory
processing
Modelling and
assessment
Plan and
execute

---
Behaviour plans
(version for the rsewiki)
Robobot level 3 (Vision)
Sensory
processing
Modelling
Behaviour generation
Behaviour
sequence
(main)
Situation
detect
Python
(socket-base-py)
Behaviour
(bplanXX)
Camera
(via USB)
Python i/f
(spyvision)
Golf ball
(m???)
Logfiles
(for Matlab)
Camera
(scam)
Aruco
(maruco)
Selected
Drive type and
parameters
Parameters
(uservice)
Most block text in brackets
corresponding to filenames
(eg. scam = scam.cpp scam.h)
---- Dashed frame means
not provided.
Config.
(robot.ini)
Drive
sensor
Drive
model
Drive
control
Level 1+2
Situation
sensor
Situation
detect
Situation
behaviour
Drive type
control
Drive
methods
Drive
sensing
Pose
sensing
Robot
pose
Drive
control
sense
Drive system
Sensory
processing
Modelling and
assessment
Plan and
execute

---
Situation detect
Snow, rain
Traffic situation
(Battery) power low
Road surface (soft, wet)
Localization lost
Someone in distress
Behavior rules (e.g. traffic)
Load status
Weed detect
opportunity
Task generate
deliver opportunity
pick up opportunity
cut weed
clean
assist/help
map
recharge option
Robot
Objective
Detect
Situation
Plan
Architecture – higher levels?
Example
Objective
plan
Calendar
access
Calendar
assess
go
Explore
plan
Map
validity
priority
e.g.
battery
Asset
projection
Recharge
plan
Asset
sense
Action
decision
Cable or net
Danger
detect
Area
limitations
Brush
use risc
Situation
items
Area
situation
Test setup
People
detect
People
movement
Friendly
behaviour
Mapping
localization
Map
route
Obstacle
sense
Local
map
Obstacle
avoid
NASREM
Pose
sense
Robot
state
Drive
control
sense
Action

---
NASREM software model
- for autonomous robot
Sensor processing
(prepare data)
World model
(in context)
Behavoiur
generation
Mission
objective
Situation
sensor
Situation
state
Behaviour
decision
Obstacle
sensor
Obstacle
map
Obstacle
avoidance
Pose
sensor
Robot
state
Drive
control
Actuator
Sensor
Abstraction
Function
Configuration and monitoring
Update frequency